## Slide 1: Drones & UAV’s
ArcGIS Local Government Showcase
9/14/17
Stoughton, WI
By: Jonathan Hodel, PE, GISP
Cloudpoint Geographics, Inc

## Slide 2
UAVs are programmed to fly a course at a set elevation. At a predetermined time interval, photographs are taken. These photos overlap enough to create a seamless image compiled of the collage of pictures.
Creating Imagery from UAV’s

## Slide 3
Amount of overlap can vary from 70-90%. Typical project site involving 150 acres may require 1,000 photos or more. Automated flight controller apps help trigger photo times & based upon GPS location.
Creating Imagery from UAV’s

## Slide 4
By utilizing GCP’s, data accuracy can be increased to 1-2 inches as opposed to 3 feet or more in native georeferencing.
Avoid obstructions
Flat spots
Color contrast
Why incorporate GCP’s?

## Slide 5
GPC’s are collected with high-accuracy, survey grade GPS. Points are then imported into the image processing software.
GPS your GPC’s, for better GIS

## Slide 6
After control points are collected and the aerial photography is brought into the system, points are manually selected from multiple photos to get achieve the high accuracy results.
So how are GCP’s used?

## Slide 7
High-res imagery
Topography
Volume calcs
Point clouds
How can this data be used?

## Slide 8
By utilizing UAVs to calculate volume, a quarry or gravel pit can better manage their inventory and stockpiles with increased accuracy and efficiency.
Applications for UAV’s

## Slide 9: Elevation Model

## Slide 10: Elevation Model

## Slide 12
County assessors can utilize drone imagery to see if any structures have been built without documentation and proper permits thus resulting in more revenue via taxes.
Applications for UAV’s

## Slide 13
In the future it is predicted that UAVs will be used in emergency responses such as post hurricane devastation, wild fires, tornadoes, and much more. This will allow organizations the ability to better track damage and create response plans.
Applications for UAV’s

## Slide 14
Need your own drone?

## Slide 15
Type of Drones

## Slide 16
Types of Drones
Source: www.dronedeploy.com

## Slide 17
DJI Phantom 4 Pro
Cost = $1,500
Flight Time = 28 minutes
Coverage = 150 acres
Camera = 20MP Exmor
Max Speed = 44 mph
Primary use: ameture videography & imagery

## Slide 18
DJI Inspire 1
Cost = $2,800
Flight Time = 18 minutes
Coverage = 100 acres
Camera = 12MP & 16MP
Max Speed = 49 mph
Primary use: videography & inspection work

## Slide 19
DJI Spreading Wings S1000
Cost (package)= $8,900
Flight Time = 15 minutes
Coverage = 100 acres
Camera = Professional grade
Max Speed = 58 mph
Primary use: Professional photos & industrial applications

## Slide 20
Event 38: E384
Cost (package)= $3,300
Flight Time = 100 minutes
Coverage = 400 acres
Camera = 18-28 MP
Max Speed = 29 mph
Primary use: surveying & mapping
Assembly video

## Slide 21
Sensefly Ebee RTK
Cost (package)= $25k
Flight Time = 40 minutes
Coverage = 300 acres
Camera = 20 MP
Max Speed = 40 mph
Primary use: Surveying & mapping
Takeoff video

## Slide 22
Trimble UX5
Cost (package)= $50k
Flight Time = 50 minutes
Coverage = 400 acres
Camera = 24 MP
Max Speed = 50 mph
Primary use: surveying & mapping
Photo of launch

## Slide 23
Firefly6
Cost (package)= $7,500
Flight Time = 45 minutes
Coverage = 400 acres
Camera = 24 MP
Max Speed = 40 mph
Primary use: surveying & mapping

## Slide 24
Let application drive the purchase decision (ag, site survey, inspection work, etc.)
Use popular flight controllers and platforms
Spend twice as much time choosing the sensor package as you are for the bird
Can the platform carry different types of sensors
Choosing the right drone

## Slide 25
FAA Registration

## Slide 26
Equipment Checklist
Batteries
Chargers
SD card
Firmware
Sunshade
Props
Data transfer tools

## Slide 27
Pix 4D
Drone Deploy Drone2Map
Agisoft
Different UAV processing tools

## Slide 28
UAVs are continuously becoming more powerful, efficient, and cheaper to operate.
If you are in the geospatial field, odds are that you are going to be utilizing UAVs throughout your careers.
Why should you care?

## Slide 29
Who’s using drones the most?

## Slide 30
Utilizing drones for this manner is beneficial in multiple ways. One main advantage is the tremendous saving of time spent for jobs. What used to take days to complete, now takes hours.
Why is this important?

## Slide 31
As the technology continues to improve, the cost savings and enhanced data collection will continue to improve as well. Jobs that used expensive planes in the past are now able to be done via UAV.
Why is this important?

## Slide 32
FAA Remote Pilot Certification
60 questions
2 hours
FAA Exam site
Valid for 2 years
Remotepilot101
How to become a UAS pilot?

## Slide 33
Project Portfolio
This map shows a collection of recent drone flights and was inserted using the Esri Maps for Office accessing a web map through our ArcGIS Online organizational account.
John Nolen Dr

## Slide 34: Questions??
Jon Hodel
Cloudpoint Geographics, Inc
jhodel@cloudpointgeo.com
877-377-8124